## Slide 1: Cache
Compiled by:
Sarosh shahid

## Slide 2: Cache Miss
Find data in cache
MOV AL, [08]
00 | 47
01 | 25
02 | 5
03 | 6
04 | 88
05 | 99
06 | 21
07 | 58
08 | 57
09 | 98
0A | 65
0B | 22
Processor
Cache
Not Found
Memory
CACHE MISS
Place 57 in
cache
57
57
Find data in memory

## Slide 3: Cache Hit
Find data in cache
MOV AL, [08]
00 | 47
01 | 25
02 | 5
03 | 6
04 | 88
05 | 99
06 | 21
07 | 58
08 | 57
09 | 98
0A | 65
0B | 22
Processor
Cache
Found
Memory
CACHE HIT
Data 57 in
cache
57

## Slide 4: Cache Miss
MOV AL, [08]
00 | 47
01 | 25
02 | 5
03 | 6
04 | 88
05 | 99
06 | 21
07 | 58
08 | 57
09 | 98
0A | 65
0B | 22
Processor
L1 Cache
Memory
L2 Cache
Find data in
L1 cache
Not Found
L1 CACHE MISS
Find data in
L2 cache
Not Found
Find data in
memory
L2 CACHE MISS
57
57
57
Place 57 in
L2 cache
Place 57 in
L1 cache

## Slide 5: Cache Miss
MOV AL, [08]
00 | 47
01 | 25
02 | 5
03 | 6
04 | 88
05 | 99
06 | 21
07 | 58
08 | 57
09 | 98
0A | 65
0B | 22
Processor
L1 Cache
Memory
L2 Cache
Find data in
L1 cache
Not Found
L1 CACHE MISS
Find data in
L2 cache
Found
L2 CACHE HIT
57
57
Data 57 in
L2 cache
Place 57 in
L1 cache

## Slide 6: Locality
Temporal Locality:
  Locality in time
  If data used recently, likely to use it again soon
  How to exploit: keep recently accessed data in higher levels of memory hierarchy
Spatial Locality:
  Locality in space
  If data used recently, likely to use nearby data soon
  How to exploit: when access data, bring nearby data into higher levels of memory hierarchy too

## Slide 7: Locality
Temporal Locality:
    If data used recently, likely to use it again soon “Variables i and a”
Spatial Locality:
    If data used recently, likely to use nearby data soon “Array A”

## Slide 8: What data is held in cache?
Ideally, cache anticipates needed data and puts it in cache
But impossible to predict future
Use past to predict future – temporal and spatial locality:
  Temporal locality: copy newly accessed data into cache
  Spatial locality: copy neighboring data into cache too

## Slide 9: Cache Performance Analysis

## Slide 10: Cache Performance Analysis
Example
Suppose a program has 2000 data access instructions (load or stores), and 1250 of these requested data values are found in the cache. The other 750 data values are supplied to the processor by main memory or disk memory. What are the miss and hit rates for the cache?
Solution

## Slide 11: Cache Terminologies
Cache Capacity C = Total number of bytes that can be stored in the cache
Data is transferred between memory and cache in blocks of fixed size called cache lines or cache blocks.
b = Block size
Block 0 | 
Block 1 | 
Block 2 | 
Block 3 | 
Block 4 | 
Block 5 | 
Block 6 | 
Block 7 | 
Cache
Cache Line

## Slide 12: Cache Terminologies
Block 0 = 4B |  |  |  | 
Block 1 = 4B |  |  |  | 
b = 32 bits = 4B
C = 64 bits = 8B
Cache
Cache Line

## Slide 13: Block Size
Block 0 | 00 | 47
 | 01 | 25
 | 02 | 5
 | 03 | 6
Block 1 | 04 | 88
 | 05 | 99
 | 06 | 21
 | 07 | 58
Block 2 | 08 | 57
 | 09 | 98
 | 0A | 65
 | 0B | 22
Block 3 | 0C | 66
 | 0D | 8
 | 0E | 55
 | 0F | 1
Memory
Block 0 = 4B |  |  |  | 
Block 1 = 4B |  |  |  | 
b = 32 bits = 4B
C = 64 bits = 8B
Cache
Cache Line
One block of cache can hold 4Bytes so memory is also logically
divided into equal chunks of 4 bytes and all 4 bytes are brought in the cache at once.

## Slide 14: Block Size
Block 0 = 4B | 57 | 98 | 65 | 22
Block 1 = 4B |  |  |  | 
b = 32 bits = 4B
C = 64 bits = 8B
Cache
Cache Line
Block 0 | 00 | 47
 | 01 | 25
 | 02 | 5
 | 03 | 6
Block 1 | 04 | 88
 | 05 | 99
 | 06 | 21
 | 07 | 58
Block 2 | 08 | 57
 | 09 | 98
 | 0A | 65
 | 0B | 22
Block 3 | 0C | 66
 | 0D | 8
 | 0E | 55
 | 0F | 1
MOV AL, [09]
Instead of bringing only [09] will bring the whole block in the cache
Block size = 4B so will bring 4Bytes and as the address [09] is in “Block 2” and it maps to the “yellow colored” block of the cache… (Spatial Locality)

## Slide 15: Offset Bits
Offset | 00 | 01 | 10 | 11
Block 0 = 4B | 57 | 98 | 65 | 22
Block 1 = 4B |  |  |  | 
B = 32 bits = 4B
C = 64 bits = 8B
Cache
Cache Line
Block 0 | 00 | 47
 | 01 | 25
 | 02 | 5
 | 03 | 6
Block 1 | 04 | 88
 | 05 | 99
 | 06 | 21
 | 07 | 58
Block 2 | 08 | 57
 | 09 | 98
 | 0A | 65
 | 0B | 22
Block 3 | 0C | 66
 | 0D | 8
 | 0E | 55
 | 0F | 1
MOV AL, [09]
Offset bits are used to identify the data
[09] is at offset “01b or 1”
[0A] is at offset “10b or 2” and so on

## Slide 16: Cache Terminology
Capacity (C):
  number of data bytes in cache
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 17: Cache Types
Set # 0 | 
Set # 1 | 
Set # 2 | 
Set # 3 | 
Set # 4 | 
Set # 5 | 
Set # 6 | 
Set # 7 | 
Set # 0 | 
Set # 1 | 
Set # 2 | 
Set # 3 | 
Set # 0 | 
Set # 0 | 
Set # 1 | 
Direct Mapped Cache
N-way Associative Cache
Fully Associative Cache
Four-way Associative Cache
Two-way Associative Cache
One-way Associative Cache
1 block per set
N blocks per set
All cache blocks in one set

## Slide 18: Design Cache
b = 4B
C = 64B
N = 1 (Direct Mapped)
  B = C/b = 16
S = B/N = 16/1 = 16
Offset Sets | 00 | 01 | 10 | 11
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
…….. |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 

## Slide 19: Design Cache
b = 32B
C = 128B
N = 1 (Direct Mapped)
  B = C/b = 128/32 =4
S = B/N = 4/1 = 4
Offset Sets | 00000 | 00001 | 00010 | ….. | 11110 | 11111
00 |  |  |  |  |  | 
01 |  |  |  |  |  | 
10 |  |  |  |  |  | 
11 |  |  |  |  |  | 

## Slide 20: Design Cache
b = 4B
C = 32B
N = 4 (4-way associative)
  B = C/b = 32/4 =8
S = B/N = 8/4 = 2
Offset Sets | 00 | 01 | 10 | 11
0 |  |  |  | 
1 |  |  |  | 

## Slide 21: Design Cache
b = 8B
Full Associative Cache
Single set with 4-ways
  C = 8B * 4 (ways) = 32B
  B = C/b = 32/8 = 4
S = B/N = 4/4 = 1
Offset Sets | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
0 |  |  |  |  |  |  |  | 

## Slide 22: Cache Terminologies
Tag Bits - A unique identifier for a group of data. Because different regions of memory may be mapped into a single block, the tag is used to differentiate between them.
We need to add tags to the cache, which supply the rest of the address bits to let us distinguish between different memory locations that map to the same cache block.
Valid bit (V)- A bit of information that indicates whether the data in a block is valid (1) or not (0).
  At the very start, the cache is empty and does not contain valid data.
  We should account for this by adding a valid bit for each cache block.
  When the system is initialized, all the valid bits are set to 0. When data is loaded into a particular cache block, the corresponding valid bit is set to 1.

## Slide 23: Example 01
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 0 |  |  |  |  | 
101 | 0 |  |  |  |  | 
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0x014
0000 0001 0100
Tag Bits Set bits Offset bits
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 0 |  |  |  |  | 
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
1
Cache Miss = 1 Cache Hit = 0

## Slide 24: Example 01
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0xFF0
1111 1111 0000
Tag Bits Set bits Offset bits
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 0 |  |  |  |  | 
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Cache Miss = 2 Cache Hit = 0

## Slide 25: Example 01
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0x0F7
0000 1111 0111
Tag Bits Set bits Offset bits
Data already present in the set “101”. To check whether it’s the same data we need “compare the tag bits”. As
0000000 ≠ 0000111 It means we have to replace the data.
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000000 | 00 | 00 | 00 | 14
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000111 | 00 | 00 | 00 | F7
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Cache Miss = 3 Cache Hit = 0

## Slide 26: Example 01
Convert to
binary
b = 4B
C = 32B
N = 1 (Direct Mapped)
Addresses are 12 bits
  B = C/b = 8
S = B/N = 8/1 = 8
Processor Memory Access Sequence
0x014
0xFF0
0x0F7
0xC03
000 | 00000000
004 | 00000004
008 | 00000008
00C | 0000000C
010 | 00000010
014 | 00000014
018 | 00000018
01C | 0000001C
020 | 00000020
……. | 
FF4 | 00000FF4
FF8 | 00000FF8
FFC | 00000FFC
Memory
Cache
0xC03
1100 0000 0011
Tag Bits Set bits Offset bits
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 0 |  |  |  |  | 
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000111 | 00 | 00 | 00 | F7
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Sets | V bit | Tags | 00 | 01 | 10 | 11
000 | 1 | 1100000 | 00 | 00 | 0C | 03
001 | 0 |  |  |  |  | 
010 | 0 |  |  |  |  | 
011 | 0 |  |  |  |  | 
100 | 1 | 1111111 | 00 | 00 | 0F | F0
101 | 1 | 0000111 | 00 | 00 | 00 | F7
110 | 0 |  |  |  |  | 
111 | 0 |  |  |  |  | 
Cache Miss = 4 Cache Hit = 0

## Slide 27: LRU bit
Least recently used (LRU) replacement: the least recently used block in a set evicted in case of N-associative and fully associative caches.
In case of 2-way associative cache, 1-bit is required to keep check of recently used data block.
  When a block is accessed its LRU bit will be set to zero (now it’s the least recently used data) and increment all the other values of LRU bit accordingly.
  When data is to be evicted from a block, replace the block with maximum value of LRU bit (1 in 2-way associative, 3 in 4-way associative and so on).
LRU bit | Data block
01 | D0
00 | D1
11 | D2
10 | D3
Example : Set “i” of a 4-way associative cache
The LRU bit indicates the sequence of memory access only for this particular set was in order –
D2 D3 D0 D1
And D1 with the least LRU bit value is the most recently accessed

## Slide 28: LRU bit
Least recently used (LRU) replacement: the least recently used block in a set evicted in case of N-associative and fully associative caches.
LRU bit | Data block
01 | D0
00 | D1
11 | D2
10 | D3
Example : Set “i” of a 4-way associative cache
LRU bit | Data block
10 | D0
01 | D1
11 | D2
00 | D3
After the data D3 is accessed again
Set the least recently used D3 to 0 and increment all the remaining bit accordingly

## Slide 29: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0xFF
1111 1111
Tag Bits Set bits Offset bits
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 0 |  |  |  | 
 | 0 |  |  |  | 
Cache Miss = 1 Cache Hit = 0
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 11111 | FE | FF
 | 0 |  |  |  | 

## Slide 30: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0x96
1001 0110
Tag Bits Set bits Offset bits
Cache Miss = 2 Cache Hit = 0
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 11111 | FE | FF
 | 0 |  |  |  | 
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 1 | 11111 | FE | FF
 | 1 | 0 | 10010 | 96 | 97

## Slide 31: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0x1E
0001 1110
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 0
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 1 | 11111 | FE | FF
 | 1 | 0 | 10010 | 96 | 97
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 00011 | 1E | 1F
 | 1 | 1 | 10010 | 96 | 97

## Slide 32: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0x97
1001 0111
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 1
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 00011 | 1E | 1F
 | 1 | 1 | 10010 | 96 | 97
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 1 | 00011 | 1E | 1F
 | 1 | 0 | 10010 | 96 | 97

## Slide 33: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0x07
0000 0111
Tag Bits Set bits Offset bits
Cache Miss = 4 Cache Hit = 1
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 1 | 00011 | 1E | 1F
 | 1 | 0 | 10010 | 96 | 97
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 00000 | 06 | 07
 | 1 | 1 | 10010 | 96 | 97

## Slide 34: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
Memory
Cache
0x06
0000 0110
Tag Bits Set bits Offset bits
Cache Miss = 1 Cache Hit = 0
Set | V bit | LRU bit | Tags | Data
 | 1 | 00 | 0000 0110 | 06
 | 0 |  |  | 
 | 0 |  |  | 
 | 0 |  |  | 
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF

## Slide 35: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
Memory
Cache
0xEF
1110 1111
Tag Bits Set bits Offset bits
Cache Miss = 2 Cache Hit = 0
Set | V bit | LRU bit | Tags | Data
 | 1 | 01 | 0000 0110 | 06
 | 1 | 00 | 1110 1111 | EF
 | 0 |  |  | 
 | 0 |  |  | 
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF

## Slide 36: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
0xB2
Memory
Cache
0xB2
1011 0010
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 0
Set | V bit | LRU bit | Tags | Data
 | 1 | 10 | 0000 0110 | 06
 | 1 | 01 | 1110 1111 | EF
 | 1 | 00 | 1011 0010 | B2
 | 0 |  |  | 
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF

## Slide 37: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
0xB2
0x06
Memory
Cache
0x06
0000 0110
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 1
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF
Set | V bit | LRU bit | Tags | Data
 | 1 | 00 | 0000 0110 | 06
 | 1 | 10 | 1110 1111 | EF
 | 1 | 01 | 1011 0010 | B2
 | 0 |  |  | 
Respective tag found so it’s a cache hit

## Slide 38: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
0xB2
0x06
0x59
Memory
Cache
0x59
0101 1001
Tag Bits Set bits Offset bits
Cache Miss = 4 Cache Hit = 1
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF
Set | V bit | LRU bit | Tags | Data
 | 1 | 01 | 0000 0110 | 06
 | 1 | 11 | 1110 1111 | EF
 | 1 | 10 | 1011 0010 | B2
 | 1 | 00 | 0101 1001 | 59

## Slide 39: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
0xB2
0x06
0x59
0x23
Memory
Cache
0x59
0010 0011
Tag Bits Set bits Offset bits
Cache Miss = 4 Cache Hit = 1
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF
Set | V bit | LRU bit | Tags | Data
 | 1 | 10 | 0000 0110 | 06
 | 1 | 00 | 0010 0011 | 23
 | 1 | 11 | 1011 0010 | B2
 | 1 | 01 | 0101 1001 | 59

## Slide 40: Types of Cache Misses
Compulsory Miss:
The first request to a cache block is called a compulsory miss, because the block must be read from memory regardless of the cache design.
Capacity Miss:
Capacity misses occur when the cache is too small to hold all concurrently used data.
Conflict Miss:
Conflict misses are caused when several addresses map to the same set and evict blocks that are still needed.

## Slide 41: Cache Parameters
  Increasing cache capacity can reduce conflict and capacity misses, but it does not affect compulsory misses.
  Increasing block size could reduce compulsory misses (due to spatial locality). But as block size increases, the number of sets in a fixed-size cache decreases, increasing the probability of conflicts.
  An N-way set associative cache reduces conflicts by providing N blocks in each set where data mapping to that set might be found. Each memory address still maps to a specific set, but it can map to any one of the N blocks in the set. However, set associative caches are usually slower and somewhat more expensive to build

## Slide 42: Cache Write Policies
Implemented to handle writes
Hit Policy
      Two methods to handle writes if the data is already present in the cache.
            Write Through
            Write Back
Miss Policy
      Two methods to handle writes if the data is not present in the cache.
            Write Allocate
            Write Around

## Slide 43: Write Through
  Update cache as well as memory
  Advantage: - read miss never results in writes to main memory - easy to implement - main memory always has the most current copy of the data (consistent) Disadvantage: - write is slower - every write needs a main memory access
  Example: Set bits = 3; Tag bits = 5; Offset bits =0; Address bits = 8
Set | Tag bits | Data
….. |  | 
100 | 10100 | 45
….. |  | 
…… | 
0C | 99
….. | 
A4 | 45
A5 | 27
…… | 
Processor
MOV [A4], 68 MOV AL, [0C]
Hit
Update both cache and memory
Set | Tag bits | Data
….. |  | 
100 | 10100 | 68
….. |  | 
…… | 
0C | 99
….. | 
A4 | 68
A5 | 27
…… | 

## Slide 44: Write Through
  Update cache as well as memory
  Advantage: - read miss never results in writes to main memory - easy to implement - main memory always has the most current copy of the data (consistent) Disadvantage: - write is slower - every write needs a main memory access
  Example: Set bits = 3; Tag bits = 5; Offset bits =0; Address bits = 8
Set | Tag bits | Data
….. |  | 
100 | 10100 | 45
….. |  | 
…… | 
A2 | 45
A3 | FF
A4 | 73
A5 | 27
…… | 
Processor
MOV [A4], 68 MOV AL, [0C]
Set | Tag bits | Data
….. |  | 
100 | 10100 | 68
….. |  | 
…… | 
0C | 99
….. | 
A4 | 68
A5 | 27
…… | 
Miss
Set | Tag bits | Data
….. |  | 
100 | 00001 | 99
….. |  | 

## Slide 45: Write Back
Update cache only. Update memory only in case of data eviction and a dirty bit is used. This status bit indicates whether the block is dirty (modified while in the cache) or clean (not modified). If it is clean the block is not written on a miss.
Advantage: - writes occur at the speed of the cache memory - multiple writes within a block require only one write to main memory - as a result uses less memory bandwidth Disadvantage: - harder to implement - main memory is not always consistent with cache - reads that result in replacement may cause writes of dirty blocks to main memory
…… | 
0C | 99
….. | 
A4 | 45
A5 | 27
…… | 
Processor
MOV [A4], 68 MOV AL, [0C]
Hit
Set | Dirty bit | Tag bits | Data
….. |  |  | 
100 | 0 | 10100 | 45
….. |  |  | 
Update only cache and set dirty bit to 1
Set | Dirty bit | Tag bits | Data
….. |  |  | 
100 | 1 | 10100 | 68
….. |  |  | 

## Slide 46: Write Back
Update cache only. Update memory only in case of data eviction and a dirty bit is used. This status bit indicates whether the block is dirty (modified while in the cache) or clean (not modified). If it is clean the block is not written on a miss.
Advantage: - writes occur at the speed of the cache memory - multiple writes within a block require only one write to main memory - as a result uses less memory bandwidth Disadvantage: - harder to implement - main memory is not always consistent with cache - reads that result in replacement may cause writes of dirty blocks to main memory
…… | 
0C | 99
….. | 
A4 | 45
A5 | 27
…… | 
Processor
MOV [A4], 68 MOV AL, [0C]
Miss
Set | Dirty bit | Tag bits | Data
….. |  |  | 
100 | 1 | 10100 | 68
….. |  |  | 
As dirty bit is 1, before eviction update the memory
Update the memory
…… | 
0C | 99
….. | 
A4 | 68
A5 | 27
…… | 
Place [0C] in cache
Set | Dirty bit | Tag bits | Data
….. |  |  | 
100 | 0 | 00001 | 99
….. |  |  | 

## Slide 47: Write Allocate
  Bring data in the cache
  Example: Set bits = 3; Tag bits = 5; Offset bits =0; Address bits = 8
Set | Tag bits | Data
….. |  | 
100 | 10100 | 45
….. |  | 
…… | 
0C | 99
….. | 
A4 | 45
A5 | 27
…… | 
Processor
MOV [0C], 68
Miss
Bring data in cache
Set | Tag bits | Data
….. |  | 
100 | 00001 | 68
….. |  | 
…… | 
0C | 68
….. | 
A4 | 45
A5 | 27
…… | 

## Slide 48: Write Around
  Also called Write No-Allocate
  Update data block in memory
  Example: Set bits = 3; Tag bits = 5; Offset bits =0; Address bits = 8
Set | Tag bits | Data
….. |  | 
100 | 10100 | 45
….. |  | 
…… | 
0C | 99
….. | 
A4 | 45
A5 | 27
…… | 
Processor
MOV [0C], 68
Miss
Update memory
Don’t bring data in cache
…… | 
0C | 68
….. | 
A4 | 45
A5 | 27
…… |